## Slide 1: DELIVERY BOT – CYBER TITANS AUTONOMOUS DELIVERY SYSTEM
M. SHREEMATHI
S. SANDHIYA

## Slide 2: Problem statement
Generally, we waste time carrying small items between rooms and departments. Manual delivery is repetitive, slow, and can cause delays. A contactless, automated delivery mechanism that safely hands over items would save time and reduce workload.

## Slide 3: OBJECTIVE
The objective is to design and build a line-following delivery bot that:
Follows a pre-marked path automatically.
Carries a small box on top and opens a single flap using a servo when at the delivery spot.Delivers items in a safe, contactless, and reliable way.

## Slide 4: Components Used
IR sensors — to detect and follow the line.
Arduino — main controller.
Motor driver DRV8833— to drive DC motors.
DC motors and chassis — movement platform.
Li ion battery— power source.
Micro servo (e.g., SG90/9g) — to open the box flap.
Small box / tray mounted on top — to hold the load.

## Slide 5: WORKING PRINCIPLE
IR sensors detect contrast between the marked line and the floor and send signals to the Arduino. The controller processes these signals and commands the motor driver to steer left, right or straight so the bot follows the path. When the bot reaches the delivery point (detected by a pre-marked stop line), the Arduino sends a PWM signal to the servo. The servo rotates the flap or lid open briefly to allow the item to be taken, then closes it and the bot can return or wait.

## Slide 6: WHAT IS INNOVATIVE
Traditional Delivery Bots usually just follow a line and stop at a destination. The user has to manually remove the item from the top of the bot.
Our Delivery Bot adds a servo-operated delivery box. At the delivery spot, the servo rotates and opens a flap of the box so that the item can be taken or automatically dropped off.
What’s innovative?
1. Contactless Handover: No need to touch the bot itself — only the opened box flap.
2. Automated Item Release: Items can be dropped at the destination without human help.
3. Secure Transport: Box remains closed during travel, preventing items from falling.
4. Scalable Design: Same mechanism can be extended to multiple delivery points with coded signals for servo action

## Slide 7
Features: the bot follows a fixed path, securely carries small items, and performs controlled flap opening using a servo at the delivery point
Advantages: reduces manpower, provides contactless delivery, and is low cost and easy to build.
Future Scope: add ultrasonic obstacle avoidance, Wi-Fi or Bluetooth control, mobile app unlocking, video feedback, or a more secure latch mechanism for valuable payloads.

## Slide 8: THANK YOU