## Slide 1: DELIVERY BOT – CYBER TITANS REMOTE CONTROLLED DELIVERY SYSTEM
M.SHREEMATHI
SANDHIYA

## Slide 2: Problem statement
In today’s world, delivery systems have become an essential part of daily life. However, most existing delivery bots face limitations in terms of flexibility and security. Line-following delivery bots are restricted to fixed paths. One major concern is the safety of the package, as there is no mechanism to check whether the delivery box has been tampered with or opened before reaching its destination. These gaps highlight the need for a system that provides both control and security while keeping costs affordable.

## Slide 3: OBJECTIVE
The primary objective of our project is to design and implement a Remote-controlled delivery bot that ensures both efficiency and safety. We aim to provide a solution where the user can navigate the bot in real time with the help of a camera, while also maintaining the security of the package using an ultrasonic sensor. The objective is not only to enable smooth transportation of items but also to guarantee that the box remains closed until the bot reaches the delivery point. In this way, our goal is to bridge the gap between convenience, control, and trust in small-scale delivery systems.

## Slide 4: Components Used
HC-05 Bluetooth module — for remote control
Arduino — main controller.
Motor driver DRV8833— to drive DC motors.
DC motors and chassis — movement platform.
Li ion battery— power source.
Esp 32 cam —live streaming to delivery.
Small box / tray mounted on top — to hold the load.
Ultrasonic sensor – To detect the presence of box.

## Slide 5: WORKING PRINCIPLE
The working principle of our delivery bot is simple yet effective. The bot is navigated remotely by the user through either a mobile application. A camera mounted on the bot provides live streaming, allowing the user to see the path and guide the bot to its destination. The package is stored in a box fitted on top of the bot. An ultrasonic sensor monitors the lid of the box by detecting the distance. If the lid is in its normal closed position, the sensor records a constant reading. This ensures that any unauthorized attempt to open the box is instantly identified, making the system secure as well as practical

## Slide 6: WHAT IS INNOVATIVE
What makes our project innovative is the integration of a live monitoring system with an intelligent security mechanism in a compact and cost-effective delivery bot.
Unlike traditional bots that simply carry goods from one place to another, our design adds a layer of trust and transparency through its camera and ultrasonic detection system.
This innovation lies in ensuring package safety without relying on complex or expensive technologies.
The bot is not just a delivery tool, but also a surveillance and security unit that reassures both the sender and the receiver that the package remains untouched throughout the delivery.

## Slide 7
Our delivery bot stands out because of the features and advantages it provides.
The remote-control capability offers complete flexibility, allowing the bot to move freely in different environments instead of being restricted to predefined paths.
The camera gives users the confidence of real-time monitoring, while the ultrasonic sensor ensures that the package remains protected until the delivery is complete.
Together, these features make the bot both practical and secure. The advantage of our system lies in its low cost, adaptability, and reliability, which make it suitable for small-scale delivery applications where safety and control are of utmost importance.

## Slide 8: THANK YOU